Memory Organization and Buffer Construction for GPGPU for 2D Physics
A presentation by:
Scott Young
A presentation to the Department of Computer Science
in partial fulfilment of the requirements for the degree of
Bachelor of Science (Honours in Software Engineering)

---
Outline
- 2D Physics with Circles
- Parallelism
- Memory Model for OpenCL
- Component Wise Addition
- Position Updating
- Collision Detection
- Collision Resolution
- Collision Information Buffer
- Strategies 0, 1, and 2
- Results
- References

---
2D Physics With Circles
- Circles have a position
- Circles have a radius
- Circles have a mass
- Circles have a velocity
- Circles exist within the arena
Figure 1

---
Parallelism
Every Circle moves based on it's velocity, acceleration, position, and whether it has hit a wall or not. Therefore position updates are parallel in the number of circles.
Figure 2

---
Parallelism
Collision detection and resolution works on pairs of circles. The information required is unique to every pair of circles.
Figure 3

---
Memory model for OpenCL
- OpenCL Uses a Streaming Memory Model
- Each Work Item has a unique global index and local index
- Parallelism is achieved by taking advantage of this structure
Figure 4 [1]

---
Component wise addition
__kernel void add_floats(__global float* a,
        __global float* b,
        __global float* out,
        int n)
{
    int i = get_global_id(0);
    if( i >= n ){
        return;
    }
    out[i] = a[i] + b[i];
}

---
Position updating
__kernel void update_position(__global float4* circle,
        __global float2* velocities,
        __global float2* gravity,
        int circles,
        float time_step,
        float restitution)
{
    int i = get_global_id(0);
    if(i >= circles){ return; }
    float2 newPosition = circle[i].xy + velocities[i]*time_step + 0.5f*gravity[0]*time_step*time_step;
/*calculate the change from any wall bounces and store in changeFromWallBounce*/
circle[i].xy = newPosition;
velocities[i] = restitution*newSpeed + changeFromWallBounce;

---
Collision Detection
__kernel void detect_collisions(__global float4* circle,
        __global float2* collision,
        int potential_collisions, int circles)
{
    int c = get_global_id(0);
    int i = 0;
    int j = 0;
    if(c >= potential_collisions){ return; }
    collision[c].xy = (float2)( 0.0f, 0.0f );
    //calculate the indexes for i and j and store in pair
    i = pair.s0; j = pair.s1;
    float min_distance = circle[i].z + circle[j].z;
    float2 distance_vector = circle[j].xy - circle[i].xy;
    float distance =
        native_sqrt( dot( distance_vector, distance_vector ) );
    if(distance < min_distance){
        float2 normal = distance_vector/distance;
        collision[c] = (min_distance-distance)*normal;
    }
}

---
Collision Resolution
__kernel void resolve_collisions(__global float4* circle, __global float2* collision,
        __global float2* velocities,
        int potential_collisions,
        int circles, float restitution)
{
    int c = get_global_id(0);
    if(c >= potential_collisions){ return; }
    float2 mtv = collision[c];
    float mtv_length = native_sqrt( dot( mtv, mtv ) );
    if( mtv_length == 0 ){ return; }
    //calculate the pair of indexes
    int i = pair.s0; int j = pair.s1;
    float2 posI = circle[i].xy - 0.5f*mtv;
    float2 posJ = circle[j].xy + 0.5f*mtv;
    circle[i].xy = posI; circle[j].xy = posJ;
    float invMassI = 1/circle[i].s3;
    float invMassJ = 1/circle[j].s3;
    float inverseMassSum = invMassI + invMassJ;
    float2 normal = mtv/mtv_length;
    float2 Vij = velocities[i] - velocities[j];
    float J = (-(1+restitution)*dot(Vij, normal))/(inverseMassSum);
    velocities[i] = velocities[i] + J*invMassI*normal;
    velocities[j] = velocities[j] - J*invMassJ*normal;
}

---
Collision Information Buffer
- The physics engine needs a way to store collision information
- For every pair of objects (i, j) there must be exactly 1 collision.
- Access times need to be fast in order for the system to handle all the collisions quickly
Figure 5

---
Strategy 0
- The i value can be calculated by solving
  for
- If ii is it's own greatest integer part
- Else
- Then get j from
ii = {-2m - 1 + sqrt{(4m(m+1) - 8c - 7)}} over {-2}
m = numberOfCircles - 1
i=ii-1
i=GIP(ii)
j=c+{i(i+1)} over {2} - (i times m)+1

---
Strategy 1
An identical array could be used that will store the (i, j) pair for a given collision index, at that collision index.

---
Strategy 2
- Instead of using the previous array which grew quadratically, a linearly growing array that stores the minimum and maximum collision index for each i
- Then calculating i is a binary search through the array
Figure 6

---
Results
- The strategies were tested on the CPU and GPU
- Strategy 1 is the best strategy for CPU usage
- Strategy 0 is the best strategy for the GPU
- Strategy 2 outperformed strategy 0 on the CPU but was the worst on the GPU
Figure 7

---
Results
- The floating point indexing was inaccurate on the GPU after 2116 circles but ran without error on the CPU until crashing at 14665 circles
- Therefore strategy 1 is the preferred strategy until GPU floating point accuracy reaches CPU floating point accuracy
Figure 8

---
References
http://www.codeproject.com/KB/showcase/Memory-Spaces/image001.jpg

---
Questions?